1100°C Ashing Furnaces

Competitive Advantages

- Protected elements

- Preheated airflow

- Multiple choices of size & control

- High quality robust design for longevity

# Typical applications

- Determination of ash content is an important test procedure for process and quality control purposes;

- Food products & animal feeds are ashed to determine the indigestible ash content for regulatory reasons,

for example; animal feeds have limits on the amount of bone meal that can be added. Grain milling process

control also uses ashing to determine purity.

- Plastics are ashed to determine and verify the fill content (i.e. Tio2), and to determine catalyst breakdown

and transfer into the polymer. Catalysts may themselves be ashed to determine the extent of fouling.

- Pharmaceutical tablets and products are ashed to determine residual non-organic, indigestible fractions

and to a lesser extent as a sample prep technique for elemental analysis.

- In the petrochemical industry oil and fractions are ashed to determine metals and element(s) concentration

in the residual ash, to understand their impact on the process equipment and applications.

| 1100°C Ashing Furnaces |
| --- |
| Furnace Model | Max. Temp. (°C) | Volume options (litres) | External Dimensions (mm) Height Width Depth | T/C Type | Max Power (kW) | Furnace supply |
| AAF11/3 | 1100 | 3 | 580 370 485 | K | 2 | Single phase |
| AAF11/7 | 1100 | 7 | 650 430 740 | K | 3.9 | Single phase |
| AAF11/18 | 1100 | 18 | 705 505 675 | K | 7 | Single or 3-phase |

| Product Features |  | Product Benefits |
| --- | --- | --- |
| Protected element design |  | Prevents carbon build up on elements, which leads to short circuits and premature failure |
| High density insulation |  | Ensures long lifetime even with high carbon samples e.g coal |
| Preheated regulated airflow |  | Ensure excellent thermal uniformity throughout chamber |
| Digital PID temperature controller |  | Microprocessor based digital control delivers precise repeatable temperatures |
| Eight or twenty segment programmer option |  | Controls heating process with ramps, dwells & cooling |
| Dense refractory around chamber entrance and on furnace floor |  | Provides excellent resistance to wear and spillage |
| Vertical lift door design Double shell construction |  | Positions hot door insulation away from operator Maintains outer case temperature to BSEN 61010 |
| Door positive break safety switch |  | Isolates power to the heating elements when door is open |
| AAF11/3 has small outer cabinet size |  | Conserves bench space |
| Inconel tray(s) and loading handle |  | Enables safe & easy loading and unloading |
| Furnace chimney |  | Provides exhaust for waste gases of ashing process |